## Slide 1: Data types in C
ESC101
9th August

## Slide 2: Last class
Four types of C statements
  Declaration
  Input
  Output
  Expressions

## Slide 3: This class
C data types
Type conversions
  Implicit
  Explicit
Consequences
Related reading: Chapter 2.7-2.13

## Slide 4: Data Types in C
char
  Single character, e.g. a or C or 6 or $
int
  Bounded integers, e.g. 732 or -5
float
  Real numbers, e.g. 3.14 or 2.0
double
  Real numbers with more precision

## Slide 5: Type modifiers in C
Signed
  Range [-2N-1 , 2N-1-1]
Unsigned
  Range [0,2N-1]
Short
  Can use half the size of the normal data type
Long
  Can use double the size of the normal data type

## Slide 6: Composite data types
unsigned char (%c)
signed short int = signed short = short (%hi)
unsigned int (%u)
signed long int = signed long = long (%li)
long long (%ll)
float (%f)
double (%f or %lf)
long double (%Lf)

## Slide 7: Rocket science
First launch of the Ariane 5 rocket on 4th June 1996
Rocket lost its flight path and disintegrated 40 seconds into launch
Cost  $370 million
Fundamental cause of disaster
  Float to int data type casting

## Slide 8: Floating point representation
Have to represent three things
  sign
  Number
  Exponent
Assign some bits of memory for each
  1 bit for sign
  m for exponent
  n for mantissa

## Slide 9: Conceptual example
Consider a 4 bit memory
  What can you assign with unsigned int?
    0,1,.....15
  What can you assign with signed int?
    Use twos complement notation
    -8,-7,.... ,7
  What can you assign with float?
s
e
m
m
(-1)s * 1.m* 2e-0
1.0, 1.1, 1.2, 1.3
2.0, 2.2, 2.4, 2.6
-1.0, -1.1, -1.2, -1.3
-2.0, -2.2, -2.4, -2.6

## Slide 10: Edge cases in float representations
Has upper bound
Has lower bound
Needs special handling for special numbers
  Zero (when e and m are all zeros)
  Infinity
Exact matches can be problematic
  Is x = 0.902323?

## Slide 11
# include <stdio.h>
int main() {
float C;
float F;
C=50;
F = ((9*C)/5) + 32;
printf(“The temperature”);
printf( “ %f ”, C);
printf(“Celsius equals”);
printf(“ %f ”, F);
printf(“Fahrenheit”);
return 0;
}
temp_conversion.c
Compile and Run
The temperature
Celsius equals
122.000000
50.000000
C
F
??
??
50.000
??
Microprocessors represent real numbers using finite precision, i.e., using limited number of digits after decimal point.
Typically uses scientific notation:
12.3456789 represented as 1.23456789E+1.
122.0000
“%f” signifies that the corresponding variable is to be printed as a real number in decimal notation.
Fahrenheit

## Slide 12: IEEE 754 floating point representation

## Slide 13: Single-precision floating point representation
This is what you’re using when you are invoking float

## Slide 14: Double precision
Same logic as single precision, but with 64 bits of memory

## Slide 15: Type Conversion (Type casting)
Converting values of one type to other.
  Example: int to float and float to int (also applies to other types)
Can be implicit or explicit
  int k =5;
  float x = k; // good implicit conversion, x gets 5.0
  float y = k/10; // poor implicit conversion
  float z = ((float) k)/10; // Explicit conversion, z gets 0.5

## Slide 16: Typecasting application
int main(){
int total=100, number=50;
float percentage=0.0;
percentage=(number/total)*100;
printf("%.2f",percentage);
}
Output: 0.0
int main(){
int total=100, number=50;
float percentage=0.0;
percentage= (float) number/total *100;
printf("%.2f",percentage);
}
Output: 50.0

## Slide 17: Loss of Information!
  Type conversion may result in lost information.
  Larger sized type (e.g. float ) converted to smaller sized type (e.g. int) is undefined/ unpredictable.
  Smaller sized type (e.g. int) converted to larger type (e.g. float) may also result in loss. Take care!

## Slide 18: float to int: type conversion (result ok)
#include<stdio.h>
int main() {
float x; int y; /* define two variables */
x = 5.67;
y = (int) x; /* convert float to int */
printf(“%d”, y);
return 0;
}
Output : 5
float x;
…
(int) x;
converts the real value stored in x into an integer. Can be used anywhere an int can.

## Slide 19: float to int type conversion (not ok!)
# include <stdio.h>
int main() {
float x; int y;
x = 1.0E50; //
y = (int) x;
printf(“%d”, y);
return 0;
}
float is a larger box, int is a smaller box. Assigning a float to an int may lead to loss of information and unexpected values.
Output:
2147483647
The floating point number 1E50 is too large to fit in an integer box.
Careful when converting from a ‘larger’ type to ‘smaller’ type. Undefined.

## Slide 20: Rocket science
Rocket’s horizontal velocity was greater than older rocket’s (Ariane 4)
Inertial navigation system
  A single calculation required conversion from double to int
  Worked fine with the smaller value in Ariane 4
  Gave a garbage result for the large value in Ariane 5
Commanded engine to make an impossibly large course correction
Veered off course
  Auto-destruct sequence initialized

## Slide 21: int to float (can go wrong)
# include <stdio.h>
int main() {
int y;
y = 1000001;
printf(“%f”, (float) y);
return 0; }
Output:
1000001.000000
Result is correct
# include <stdio.h>
int main() {
int y;
y = 10000009;
printf(“%f\n”, (float) y);
printf(“ %d”, y);
return 0; }
Output:
10000008.000000
10000009
Result is not correct.
Information is lost
16 bit float vs 32 bit int

## Slide 22: char to int
Range: 0 to 255
You should NOT try to remember ASCII values
  Encoding/programming languages provide alternatives to use them
C treats characters as integers corresponding to their ASCII value.
While displaying with %c placeholder, the ASCII value is converted to its corresponding character.

## Slide 23: char  int
Interconversion between character and integer datatypes can be exploited to write programs.
printf("%d\n", 'A');
printf("%d\n", '7');
printf("%c\n", 70);
printf("%c\n", 321);
Output:
65
55
F
321 is outside range! What do you think will be the output of
printf("%c\n",321);
Try it out

## Slide 24: char-int operations
Interconversion between character and integer datatypes can be exploited to write programs.
printf("%c\n", ‘C’+5);
printf("%c\n", ‘D’ - ‘A’ + ‘a’ );
printf("%d\n", ‘3’ + 2);
Output:
H
d
53
Placeholder determines the output.
Use with caution.
Avoid arithmetic operation such as * and / on characters.
Common Mistake: Incorrect data type of placeholder.

## Slide 25: Next class
I/O
  Escape sequences etc.
Operators
  Related reading : Chapter 3